## A short conceptual introduction to STGraph
STGraph is a software system to create, edit and run models of dynamical systems. It has been designed so that the constraints to be satisfied while building models faithfully correspond to the guidelines of the so called “space state approach” of System Theory.
A model in STGraph is described as a set of variables, where the value of each of them can depend on (simulated) discrete time and on the value of one or more other variables of the model itself. All variables in the same model share the same time representation, defined by:
- initial time step of simulation (system variable time0);
- final time step of simulation(system variable time1);
- time step width of simulation (system variable timeD).
Model variables are synchronously computed in function of the system variable time, that assumes the values time0, time0+timeD, time0+2*timeD, ...
The value of each variable is computed according to a logic which depends on the type of the variable, which can be either algebraic, or state, or state with output.
- An algebraic variable has a value determined through its output function, that may consist of a constant value (such as 1 e 2+2) or of an expression depending on time (such as time^2) and/or other variables (such as x+y if x and y are variables defined in the model: in this case the dependence on time of such variables remains implicit).
  The output function is computed in a synchronic way: from the point of view of the model, the variable value is computed in the same (simulated) time step in which the values of the variables on which it depends are computed; the output function is then actually an algebraic equation.
  From the point of view of System Theory, an algebraic variable can be thought of as the simplest combinatorial system, described by a function input → output:
  h: U → Y	y(t) = h(u(t))
- A state variable has a value determined through its initial state and state transition functions, according to the following logic:
  - in the initial time of simulation, when the value of time is time0, both the initial state function and the state transition function are computed: the initial state is set to the value of the initial state function; the next state (i.e., the one when the value of time is time0+timeD) is set to the value of the state transition function;
  - in each time step, the current state is determined by the value of the state transition function computed in the previous time step, and the state transition function itself is recomputed to determine the next state, possibly also in function of the current state, denoted by the system variable this; the variable value is equal to the current state.
  The state transition function is computed in a diachronic way: from the point of view of the model, the state is computed for the (simulated) time step following the one for which the values of the variable on which it depends are computed; hence the state transition function is a finite difference equation.
  From the point of view of System Theory, a state variable can be thought of as the simplest sequential system, described by a function input ´ state → state:
  j: U ´ X → X	x(t) = j(u(t), x(t))
  given that:
  h: X → Y	y(t) = x(t)
- A state with output has a behavior analogous to the one of a state variable, with the difference that its value does not equal to the state but is determined by an output function.
  From the point of view of System Theory, a state with output variable can be thought of as the simplest dynamical system, described by a pair of functions input ´ state → state and input ´ state → output:
  j: U ´ X → X	x(t) = j(u(t), x(t))
  h: U ´ X → Y	y(t) = h(u(t), x(t))
Some simple examples may be useful to show the behavior of variables in STGraph (let us denote with x-init, x-trans, and x-out the initial state function, the state transition function, and the output function of the variable x respectively).
x algebraic:
x-out ← sin(y)	x computes the sine of the variable y
x algebraic:
x-out ← exp(time)	x computes the exponential of the system variable time
x state:
x-init ← 0
x-trans ← this+1	x computes the sequence 0, 1, 2, ...
x state:
x-init ← u
x-trans ← this	x maintains the value set at the first time step
x state:
x-init ← 0
x-trans ← u	x maintains the value received in input at the previous time step
x state with output:
x-init ← ...
x-trans ← u
x-out ← (u-this)/timeD	x computes the approximated derivative of the sequence u
x state:
x-init ← ...
x-trans ← this+u*timeD	x computes the approximated integral of the sequence u